## Slide 1: DM search with CUTE/SuperCDMS low background facilities
Serge Nagorny
on behalf of the CUTE collaboration
May 8th, 2019

## Slide 2: Dark matter evidence
Astronomical and cosmological observations suggest that
dark matter composes about 25%
of all matter in the universe
Credit: O. Lopez-Cruz
I. K. Shelton
Credit: cdms.phy.queensu.ca
Credit: NASA, CXC, Cfa, et al.

## Slide 3: Brief reminder of situation in DM search
J Masbou EDU2017

## Slide 4: Direct dark matter search
CRESST
COSINUS
HEAT/PHONONS
PICO
SCINTILLATION
IONIZATION
EDELWEISS
SuperCDMS
LUX
XENON
DarkSide
PandaX
WIMP
DAMA, SABRE, DEAP,
COSINE, MiniCLEAN,
XMASS
DAMIC, SENSEI,
NEWS-G, DRIFT, MIMac

## Slide 5: Direct dark matter search
HEAT/PHONONS
IONIZATION
SuperCDMS
WIMP
Two channels approach
allows significant improvement
of experimental sensitivity !
WIMP (~ 200 km/s) interacts by elastic scattering on nuclei
Nuclear recoil <E> 1–100 keV
Exponential distribution
Low rate 110-4 evt/kg/d

## Slide 6
Signal  DT = Eo / CT
CT = gT + AT3
Cryogenic semiconductor detectors are operated at 10-30 mK to measure energy depositions
Transition edge sensors (TESs) measure thermal energy in the form of phonons
Charge is collected on electrodes on surfaces and amplified with sensitive charge amplifiers
Measuring both phonons and charge signals allows for discrimination between electron and nuclear recoils
Concept of
ionisation-phonon detector

## Slide 7: SuperCDMS detectors
Two channels (charge & phonons) allowing for particles discrimination (nuclear or electron recoils)
Can reject events that occur near the surface
Low energy threshold due to the Luke amplification of phonon signals on drifting charges
One channel (phonons)
NO particle discrimination
NO sensitivity to surface events
iZIP detectors
HV detectors

## Slide 8: SuperCDMS detectors
Each detector of about
1 kg Ge/Si
6 detectors
in tower
Phase 1: 4-7 towers in cryostat
Final goal: 31 towers

## Slide 9: SuperCDMS setup (construction 2019-2020)
arXiv: 1610.00006

## Slide 10
DAMA
DAMA
CDMS Si
LUX 2013
DEAP
CDMS II 2015
DAMIC 2016
SuperCDMS LT 2014
CRESST
2015
CDMSlite
2015
Solar Neutrinos
Atmospheric Neutrinos
Si HV
Si iZIP
Ge HV
Ge iZIP
LZ
XENON1T 2017
Longterm goal
“iZIP” detectors
Higher threshold
Part.ID.
SuperCDMS expected sensitivity @ SNOLAB
“HV” detectors
Low threshold
No Part.ID.
arXiv:1610.00006

## Slide 11: Motivation for CUTE facility
Provide a moderate size (10 kg detector) handy (few days turnover) well-shielded cryogenics (20 mK) infrastructure for rare event physics
  Test and validation of entire SuperCDMS detector tower (6 detector + electronics)
  Measurements in a low background environment avoiding cosmogenic activation of detector’s material (3H, 32Si, etc.)
  Complete SuperCDMS detector characterization to understand its intrinsic background and noise issues
  Confirmation of screening program and handling procedures
  Early science run for dark matter search can be performed thanks to low-background environment and low-energy threshold of SuperCDMS detectors
Testing of various type cryogenic detectors

## Slide 12: SuperCDMS and CUTE at SNOLAB
SuperCDMS
2 km deep
Strong cosmic ray flux
suppression
Cleanroom environment
Rn-free air plant

## Slide 13: General view of the CUTE facility
Monorail with
1000 kg hoist
Platform
Movable
HDPE shield
UP water
shield tank
Cryostat
Cleanroom
Drywell with
Pb shield/
Mu-metal

## Slide 14: Shielding in the CUTE facility
Cryostat placed inside the drywell of a water tank
1.5 m of water layer at side and 1.0 m at bottom reduces external neutron and gamma flux
11-15 cm of low activity Pb reduces residual gammas
The gap from the top is closed off by 20 cm of HDPE and 15 cm of Pb inside cryostat
Internal Cu shields block IR photons, which contribute to detector noise

## Slide 15: PE shielding
Installed
Fully functional, tested during Pb shield installation, Jan 2019

## Slide 16: Lead shielding
Pb inner layer
< 3 Bq/kg
Pb outer layer
< 30 Bq/kg
650 kg
140 kg
2 cm
inner layer
9 cm
outer layer
13 cm
outer layer

## Slide 17: Lead shielding
Lead cover plate
Gas purge system
Serge
Inner Pb, 2 cm
< 3 Bq/kg
Mu-metal
Outer Pb, 9 cm
< 30 Bq/kg
Installed @ Jan 25th, 2019
Service step
Drywell

## Slide 18: Cleanroom (Class 500)
to minimize dust and radon exposure of detectors during mounting/dismounting procedures
Air @ SNOLAB | Underground | Surface
Rn activity | 100-130 Bq/m3 | < 10 Bq/m3
Handling time | 30-40 minutes | 8 hours
our goal
Acceptable exposure < 80 Bqh/m3
SuperCDMS detector tower will be delivered to SNOLAB in container under N2 atmosphere and must be opened and installed in cryostat at CUTE cleanroom

## Slide 19: Cleanroom
Space for two operators
Aluminum structure with LEXAN panels
Resistant to seismic events
Movable
Lifting device for cryostat cans
Low Rn air supply (< 3 Bq/m3)
Later SuperCDMS Rn-filter system (< 0.1 Bq/m3) will be used
Crane moves cryostat between cleanroom and drywell

## Slide 20: Cleanroom status
95% installation accomplishment
To be completed:
Connection to compressed air line
HEPA filter installation
Will be completed within last week of May, 2019

## Slide 21: Calibration system concept
Different radioactive sources will be used to calibrate the energy scale and to monitor stability of detectors performance, as well for characterization of particle interaction types
Gamma source: 133Ba (this Installation stage)
Neutrons source: 252Cf (next step in a while)
Sources will be remotely moved from shielded storage box to the measurement position

## Slide 22: Calibration system status @ March 1st, 2019
Guiding tube
Plastic chain
133Ba source

## Slide 23: Active two-stages suspension system
Our detectors are sensitive to mechanical vibrations
Pulse tube cooler and turbo pump are strong source of vibrations that may compromize detector performance
Both are mounted on separate plate with soft coupling (bellows) to cryostat to minimize vibrations
The bellows makes system sensitive to pressure fluctuations in SNOLAB
Active suspension system tracks/controls cryostat position better than 1 mm
Mechanical parts of the Suspension system
SS frame
Pulse tube & turbo pump

## Slide 24: Suspension system assembly
damper
supporting frame
added masses
(about 400 kg in total)
drywell
electronics box
pulse tube
turbo pump

## Slide 25
Suspension system assembly
installed at March 1st, 2019
Lowering suspension frame into drywell
Suspension frame is installed
Service handles & step
Cryostat
alignment pins
Lab jacks
Calibration
system

## Slide 26
Remote control of suspension system
Tracks environmental condition (pressure, water level, noise level)
Records of all system parameters into database
Provides possibility to off-line analysis of behavior

## Slide 27: Cryostat delivery to SNOLAB underground site
Ready to the first mechanical test in cleanroom/dry-well

## Slide 28: Payload for CUTE
Task | Time Period
Testing of CUTE facility at SNOLAB Without detectors With detectors (G124) Revision/fixing problems/commissioning | May 2019 – June 2019
Testing SuperCDMS detectors Si HV Pathfinder HVeV detector First tower (6 iZIP Ge Detector) | July 2019 – May 2020
Own R&D activity HVeV detector from enriched 28Si Scintillating bolometers based on YVO4, ZnSe, archPbMoO4 crystals Advanced light detectors | from Sept 2019
Commissioning
Early operation

## Slide 29: Background budget in energy range 0-2 keV
Material | Estimated background, events/(keVkgday)
External background (lad walls, etc.) | 1.1
External Pb shielding | 0.7
Stainless steel vacuum can | 0.6
Internal background (cryostat cans, etc.) caused mostly by 210Pb | 0.5
Cosmogenic activation (3H, etc.) | < 0.1 (SNOLAB) 0.5 (early detector)
32Si (in silicon detectors) | 0.7
Detector housing | < 0.1
Total background for Ge SuperCDMS detectors in the CUTE facility
is estimated to be  3 events/(keVkgday)
and will be precisely evaluated in the first background runs at SNOLAB

## Slide 30: Early science at CUTE facility
One Tower of HV-type SuperCDMS (6 detectors) measured for 1 year

## Slide 31
Explore the Universe with CUTE!

## Slide 33: Luke-Neganov effect in CDMSLite -2: use phonons to read charge
Bias a standard SuperCDMS 600 g iZIP detector at 69 V (rather than 4 V)
Phonon amplification proportional to charge, bias voltage
Single detector : exposure 70 kg.d
Threshold : 75 eVee = 350 eVNR on Ge
Loss of background discrimination
BG diluted with respect to signal

## Slide 34
Dark matter theories
arXiv: 1310.8642

## Slide 36: Test done @ Queen’s University
“G115”
 76 × 10 mm
240 g
4 phonon channels
TES chip
10 × 10 × 1 mm
0.5 g
4 phonon channels
RF noise/Vibration
Bolometric performance/
External background

## Slide 37: Test done @ Queen’s University
241Am source
Low energy 17.7, 20.7, 26.3 keV X-rays show good energy resolution
59.5 keV line appears at a lower energy due to detector saturation effects
Low energy events are mostly noise induced trigger, improved analysis techniques should remove most of this
241Am
X-rays
241Am
59.5 keV
noise
Ethr = 5 keV
FWHM = 1 keV @ 17.7 keV

## Slide 38: Test done @ Queen’s University
HF Noise
Before RF box
  Normal Noise: ~5 pA/√Hz
  SC Noise: ~40 pA/√Hz
The noise of TES-chip was studied
while they were in the transition between normal and superconducting states, and in normal state
An aluminum box was placed around the read-out electronics, leading to an improvement in high frequency noise
The power supply for the read-out electronics that will be used at SNOLAB was also tested, and it lead to improved high frequency noise performance as well

## Slide 39: Expected detectors for Early Operation
Si HV Pathfinder Detector
Ge iZIP Prototype Detector
6 detectors in Tower
1 detector in Tower
July 2019 – August 2019
March 2020 – May 2020

## Slide 40: Final arrangement
3/9/2016

## Slide 41: PE shielding
20 cm thick HDPE layer on top of the cryostat for neutron flux suppression

## Slide 42: PE shielding
8 layer of 1” HDPE sheet
Rigging/lifting test at producer site

## Slide 43: Calibration source design (tested)

## Slide 44: Calibration source encapsulation
as-bought
in 1st layer
in 2nd layer
Double layer encapsulated, ready to be assembled

## Slide 45: Calibration system: general overview

## Slide 46: Time-schedule
Date (week) | Task
Feb 4, 2019 | Prepare suspension frame for shipping
Feb 5th, 2019 | Installation Review Phase 2B
Feb 11, 2019 | Assemble, clean, and package of calibration system Ship suspension and calibration to SNOLAB Fix last cryostat deficiencies
Feb 18, 2019 | Clean and package cryostat Ship suspension system underground
Feb 25, 2019 | Install calibration and suspension systems
Mar 25, 2019 | Ship cryostat to SNOLAB and ship underground with CUTE staff presence
Apr 1, 2019 | Cryostat installation Preparation for Operational Readiness Review
May 2019 | Operational Readiness Review

## Slide 47: CUTE tasks before Early Operation
Date | Step
May, 2019 | DAQ mounting, and implement DAQ architecture for underground/surface CUTE lab
May, 2019 | Preparation for Operational Readiness Review
June, 2019 | Cleanroom operation test - air quality test - operational test - working procedure improvement
July, 2019 | Test all procedures , its correction based on the results of first run without/with detectors
July, 2019 | Evaluation of required manpower for run preparation&running
end of 2019 | Radio-assay of materials used for CUTE facility production
end of 2019 | Completion of CUTE background model